## Slide 1
WILDFIRE PREDICTION
Using Satellite Imagery
Association of Data Science Workshop
Monday, March 16 · 6–7 PM · Woodward 154
The big idea
Satellites measure how much light the ground reflects at different wavelengths — and fire changes those reflectances dramatically. We'll turn those raw measurements into an ML model that detects active wildfires anywhere on Earth.

## Slide 2
What We're Building Today
01
The Data
NASA fire detections + ESA Sentinel-2 spectral bands
02
Spectral Indices
NDVI, NBR, BAI, MIRBI — turning bands into fire signals
03
Train the Model
Random Forest + XGBoost on 3,500 real satellite pixels
04
Evaluate & Visualize
AUC-ROC, confusion matrix, interactive map

## Slide 3
Data Source 1: NASA FIRMS
Thermal heat detection — updated every 3 hours
NOAA-20 satellite
Orbits at ~830 km altitude, scanning Earth twice daily
How it detects fire
Measures mid-infrared radiation at 3.7 μm — fire glows intensely here, normal land is nearly invisible
bright_ti4
Brightness temperature in Kelvin. Normal land ~300 K · Active fire 330–420 K+
frp
Fire Radiative Power (MW) — total heat energy released. Brush fire ~5 MW · Major wildfire 500+ MW

## Slide 4
Data Source 2: ESA Sentinel-2
Spectral reflectance — 13 bands, 10–20 m resolution, every 5 days
What it measures
How much light the ground reflects at each wavelength — different surfaces have distinct spectral signatures
Healthy plants
Absorb red (photosynthesis via chlorophyll) · Strongly bounce near-infrared (NIR) off leaf cell structure
Fire effect
Plant structure destroyed → NIR collapses · SWIR bands B11 & B12 spike — burn scars glow at 1610–2190 nm
Why it matters
Detects fire damage even days after a fire — the spectral scar persists long after flames are out

## Slide 5
The Four Bands We Use
Surface reflectance = fraction of incoming sunlight that bounces back to the satellite (0.0 → 1.0)
B4 Red 665 nm
↑ Rises after fire
Healthy plants absorb red for photosynthesis — ash/char reflects it back
B8 NIR 842 nm
↓ Drops sharply
Healthy leaves bounce NIR off cell structure — fire destroys this immediately
B11 SWIR1 1610 nm
↑ Rises strongly
Sensitive to moisture — dry and burned vegetation reflects shortwave-IR strongly
B12 SWIR2 2190 nm
↑↑ Spikes highest
The primary fire band — flames and fresh burn scars are extremely bright at 2190 nm

## Slide 6
Spectral Indices: Amplifying the Fire Signal
Ratios between bands cancel out noise (sun angle, haze, soil) and isolate what we care about.
NDVI
Range: −1 to +1
(NIR − Red) / (NIR + Red)
Fire Drops — veg destroyed
NBR
Range: −1 to +1
(NIR − SWIR2) / (NIR + SWIR2)
Fire Goes negative — burn scar
BAI
Range: 1 to 1000+
1 / ((0.1−Red)² + (0.06−NIR)²)
Fire Spikes — active fire
MIRBI
Range: −2 to +10
10×SWIR2 − 9.8×SWIR1 + 2
Fire Rises — burning surface

## Slide 7
The Workshop Dataset
3,560 pixels · 10 real wildfire events · 2020–2023 · fire_label: 1 = fire, 0 = non-fire
Fire events included
2020
Creek Fire, CA
2021
Dixie · Caldor · Bootleg
2022
McKinney Fire, CA
2023
Canada BC + Alberta
2023
Chile · Maui · Siberia
Each row contains
FIRMS columns
latitude, longitude, acq_date
bright_ti4 (K), frp (MW), confidence
Sentinel-2 bands
B4_Red, B8_NIR, B11_SWIR1, B12_SWIR2
Spectral indices
NDVI, NBR, BAI_log, MIRBI, SWIR_ratio

## Slide 8
Training the Classifier
9 spectral-only features 75 / 25 train-test split
B4 Red
B8 NIR
B11 SWIR1
B12 SWIR2
NDVI
NBR
BAI log
MIRBI
SWIR ratio
Random Forest
200 independent trees, each trained on a random data + feature subset. Final answer = majority vote. Good for feature importance.
XGBoost
300 trees built sequentially — each corrects the previous one's mistakes. Typically higher accuracy on tabular data.

## Slide 9
Why Not Just Use Accuracy?
Only ~5–15% of satellite pixels are on fire at any time.
A model that predicts "no fire" for everything would be 85–95% accurate — but completely useless.
AUC-ROC
Separates fire from non-fire at every threshold. 1.0 = perfect, 0.5 = random. Immune to class imbalance.
Precision
Of pixels flagged as fire, what fraction are actually fire? Low = too many false alarms.
Recall
Of actual fire pixels, what fraction did we catch? Low = missed fires — the most dangerous failure.

## Slide 10
End-to-End Pipeline
1
Load dataset
3,560 pixels from 10 real fires · FIRMS schema + S2 bands + indices
2
Explore the data
Distribution plots: raw bands vs. spectral indices — see what separates
3
Engineer features
NDVI, NBR, BAI, MIRBI, SWIR ratio — cancels noise, amplifies fire signal
4
Train + evaluate
RF + XGBoost
5
Add On: Map predictions
Interactive Folium map — click any pixel for indices and probability
6
Add On: Experiment
Add thermal features (frp, bright_ti4) — watch AUC change and discuss why